## Slide 1: Food 5450M Industrial Project: Food Innovation Yogurt based food: ‘Soy yogurt drink with kiwi Flavour’ Unit III: Defining product and process specifications
Group B
Marianna Christofi
Yashorajvardhini Nimbalkar
Huiying Shang
Rong Lu
Zhun Wang

## Slide 2: Introduction
Aim : develop and optimize the final product defining the product and process specifications by:
developing the process and equipment flowchart according to legislation specifications
conducting consumer sensory and descriptive analysis

## Slide 3: Outline
Process and equipment flowcharts for both laboratory and industrial scale
Factory layout for the production process
Design experiments for conducting product & process optimisation (Screening + Optimisation)
Conduct sensory consumer & descriptive analysis
Specify product & process formulations and determine whether are in compliance with relevant legislation

## Slide 4: Laboratory Process Flowchart

## Slide 5: Laboratory Process Flowchart
2 main processes
Kiwi juice extraction
Kiwi juice extraction
Yogurt fermentation

## Slide 6: Laboratory Process Flowchart – Yogurt Fermentation
Standardised cow’s milk
Fat -1.5-1.7%
Pre-heat
Temp=42 o C, t=5-10 min
Add skimmed milk powder
Final solid content: 20-25% solids

## Slide 7: Laboratory Process Flowchart – Yogurt Fermentation
Inoculation with bacteria culture
Streptococcus thermophilus, Lactobacillus bulgaricus
Fermentation
Temp=40 -45°C, Time= 4-5 hrs
Check lactic acid content (acidity)
Till is 1.5 %

## Slide 8: Laboratory Process Flowchart – Kiwi juice extraction
Mature kiwis
Washing
With clean water
Freezing
For 30 min at -30° C
Fresh kiwi

## Slide 9: Laboratory Process Flowchart – Kiwi juice extraction
Extraction of juice
Blending for 1 -2 min
Mixing of juice and water
Deaeration
Prevention from contact with air
Sterilised water
Blending

## Slide 10: Laboratory Process Flowchart
Add sugar and soy yogurt
Blend for 1-2 min
Mixing
Hand mixer
Storage
Cold room
Time-1-2min
Temp- 4°C

## Slide 11
Industrial Flow Chart

## Slide 12: Industrial process
Industrial processing carries three lines
Cows yogurt
Soy yogurt
Kiwi juice

## Slide 13: Cows yogurt and Soy yogurt (Line 1 and 2)
Receiving of milk and storage
Checking of quality parameters
Standardization
Fat-1.5-1.7%
Pasteurisation
Temp= 62.8°C
Storage in silos at4° C
SNF- 16%
Evaporation
Improves stability and firmer structure
Time=30min
Prevents deterioration of milk
Denaturation of protein

## Slide 14: Cows yogurt and Soy yogurt (Line 1 and 2)
Homogenisation
Reducing size of fat globules
Inoculation and Fermentation
(1-2%) Streptococcus thermophilus and Lactobacillus bulgaricus
Temp=40-65⁰C
Temp=40-45⁰C
Time= 4-5 hour
convert sugar into lactic acid
pH of final yogurt=4.2-4.5
Preparation of stirred yogurt

## Slide 15: Kiwi juice (Line 3)
Receiving kiwis
Same variety and maturity
Sorting
Size, appearance
Washing
In running water with 0.1% KMNO4
Remove rotten, unripened or extremely ripened

## Slide 16: Kiwi juice (Line 3)
Drying
Cold air line
Chilling
In cold room at-18⁰C for 30min
Peeling
Outer skin of kiwi is removed
To prevent deterioration due to moisture

## Slide 17: Kiwi juice (Line 3)
Remove middle hard core part
Difficulty in blending
Cutting
Small pieces to make extraction easier
Extraction of juice
Blending
Causes bitterness
Not for longer time to avoid braking of seeds

## Slide 18: Kiwi juice (Line 3)
Coarse filtering
Uncrushed part, fine colloidal particles are removed
Mixing with water
Soft water
Standardization
pH=3.55, Acidity=0.14%, TSS= 13%
Boiled at 100⁰ C and cool to 4⁰C.

## Slide 19: Kiwi juice (Line 3)
Deaeration
Avoid contact of juice with air to prevent oxidation
Mixing
Blending of soy yogurt, cows yogurt, sugar, kiwi juice together
Checking of parameter
MSNF=8-9.5%, Fat= 1.3-1.5%, pH= 4-4.5
Stabiliser(0.01%) and citric acid(0.8%)

## Slide 20: Kiwi juice (Line 3)
Homogenisation
Disruption of particles at pressure of 6MPa
Removing air from bottles and filling
Remove Dust, dirt, air
Sealing and sterilization of bottles
Temp-40⁰C
High speed filling
Aseptic filling
Time- 2-3min

## Slide 21
Equipment

## Slide 22: Equipments Selection Principle
Capacity 5000----10000 units 2500l/day
Time
Standards
Processing requirements
CIP
GMP
HACCP
Cost

## Slide 23: Equipment
Tanks
- Storage tank
- Fermentation tank
- Multipurpose tank
Fermentation only
Tank: Fermentation/Cooling Tank
2500 Litre
Seperator
-The TS-500-0 seperator
-The final fat content of the milk process is within pre-set limits (0%- 3,5%)

## Slide 24: Equipment
Bath pasterurizer
500-1,000 L/Batch,65°C
Homogenizer
The TH-025 homogenizer ,500L per hour 0-65°C
Cooling system
The cooling system (TC-6000) temperature ranges
from 2-4°C
Filling machine
The Dogaseptic series
Blender
Gasti DOGAmix 60

## Slide 25: Equipment
Deaerator
FrymaKoruma Vacuum Deaerating Unit type VE
Labelling machine
Heat exchanger
plate heat exchanger (PHE)
tubular heat exchanger, including the multitube or multichannel designs
scraped/swept surface heat exchanger.
CIP system

## Slide 26: Regulations
Drinking yogurt-------yogurt products
Flavoured fermented milk-------not contain more than 15% of fruit
Milk protein in fermented milk and yogurt >2.7%,
Milk fat in fermented milk <10% and <15% in yogurt
Acidity (expressed as the percentage of lactic acid) of fermented milk >0.3% and 0.6% in yogurt
Sum of the microorganisms constituting started culture > 107 in both fermented milk and yogurt

## Slide 27: Regulations
Pasteurization
- Temperature>71.7°C for 15 seconds or
>62.8°C for 30 minutes then cooled to 10°C
Labelling
- List of ingredients
- Food Labelling regulation (1996)
- Allergies Information: milk, soy

## Slide 28
食品工厂设计
Factory Layout

## Slide 29: Factory Layout Design
Ensure a appropriate layout is to:
Comply with Accreditation Standard requirements
Legislative requirements
Efficient utilization of resources

## Slide 30: Plan of layout
Raw material warehouse
Production area
Packaging workshop
Refrigeration plant
Laboratory
Locker room and toilet
Electricity substation room and machine repair shop
Reserving area

## Slide 31
YOGHURT fermentation
KIWI Juice

## Slide 32: Important point for layout design
All functions should processed with no criss-crossing and backtracking
Visitors should move from clean to unclean areas
Ingredients should move from dirty and clean area as they become incorporated into food products
Conditioned air and drainage should flow from clean to dirty areas
The flow of discarded outer packaging material should not cross the flow of products
There is sufficient space for plant operations including processing, cleaning and maintenance. Space is also required for movement of materials and pedestrians

## Slide 33
Experiment design and screening experiment results

## Slide 34: Product acceptability and preference experiment design
Preference test with 9-point hedonic scale
Complete block design
The questionnaire was designed using the Compusense five
Samples were presented in balance, random, order according to randomised block design
All samples were prepared on the same day of the test with the same way, using the same raw materials, and under the same conditions
Table 1. The 9-point hedonic scale

## Slide 35
Factor | Lower limit | Upper limit
% cow’s yogurt | 7.2 | 36.5
% water | 13 | 34
% kiwi juice | 8 | 15
% sugar | 6 | 15
Table 2. Screening experiment: factors’ limits
16 samples: LLLL, LLLH, LLHL, LLHH, LHLL, LHLH, LHHL,
LHHH, HLLL, HLLH, HLHL, HLHH, HHLL, HHLH, HHHL, HHHH
The 16 samples were evaluated for overall acceptability by 32 untrained assessors in two sessions, 8 samples for each session
Product acceptability and preference experiment design

## Slide 36
Factor | Lower level (L) | Medium level (M) | High level (H)
% kiwi | 8 | 10 | 12
% cow’s yogurt | 7.2 | 14.7 | 22.2
Table 3. Optimisation experiment, factors’ limits
9 samples: LL, LM, LH, ML, MM, MH, HL, HM, HH
9 samples were examined by 54 untrained assessors in a single session
Product acceptability and preference experiment design

## Slide 37: Screening results analysis
Assessors prefer the product with low kiwi %, low cow’s yoghurt % and high % of water
The response of the assessors shows that the products with best sweetness
are those with middle percentage of sugar

## Slide 38
Optimization results analysis

## Slide 39: Optimization result analysis
Figure 1. Response surface plot for Kiwi flavor, (X1= % cow’s yogurt, X2=% kiwi juice)

## Slide 40: Optimization results analysis
Figure 2. Response surface plot for milk flavor, (X1= % cow’s yogurt, X2=% kiwi juice)

## Slide 41: Optimization results analysis
Figure 3. Response surface plot for overall acceptability, (X1= % cow’s yogurt, X2=% kiwi juice)
The best formulation for percentage of kiwi juice and cow’s yogurt is at 14.5% and 9%

## Slide 42
Product formulation and Process specification

## Slide 43: Raw material
Raw material (For 1000g drink) | Specification | Quantity
Cows yogurt | “Morrisons” low fat (1.5%) | 14.5% (145gm)
Soy yogurt | “Alpro” | 47.5% (475 gm)
Water | Sterilized tap water from lab | 20% (200gm)
Kiwi | “Morrisons” mature | 9% (90gm)
Sugar | “ Morrisons” granulated sugar | 10% (100gm)
Table 4. Raw material specification for lab scale

## Slide 44: Process specification
Time
Temperature
pH
Pressure
Hygiene
Microbiological and chemical parameters

## Slide 45: Product specification
Raw material
pH
TSS
Acidity
% of fat
SNF

## Slide 46: Packaging
Primary
Secondary
Tertiary
250 ml PET
Cartons
Crates

## Slide 47: Conclusion
Description of process and equipment flowcharts, and check if the production process is in compliance with relevant regulations
Factory layout design for the production process
Conduct product acceptability and preference test
Design experiments for conducting product & process optimisation
Determine product formulations & the process formulations

## Slide 48: Plan of action

## Slide 49
Thank you